## Slide 1: Fire Engine Driving Operations
Unit 3B - Basic Driving Skills

## Slide 2: Objectives
Describe and demonstrate the driver walk-around before moving a fire engine.
Describe the STOP procedure and how it relates to the driver when operating a fire engine.
Identify danger zones around fire engines and describe actions that can be performed to reduce risk in these areas.

## Slide 3: Objectives
Describe and demonstrate the start-up and shifting procedures an ENOP must perform when operating fire engines.
Identify hazardous driving situations and describe actions that can be performed to reduce risk.
Demonstrate on an established course fire engine handling and maneuvering capabilities.

## Slide 4: Preparing to Drive a Fire Engine

## Slide 5: Pre-trip Inspection (Preventative Maintenance Check)
Performed daily during fire season
Documented in the FEMPR
Different from the driver walk-around

## Slide 6: Driver Walk-Around
Passenger Side Front
Driver Side Front
Driver Side Rear
Passenger Side Rear
Cab

## Slide 7: Walk-Around Watch Outs
Rocks in the way of tires
Holes, berms, ditches, etc.
Large stobbs or downed trees
Chock blocks secured and in place
Gear or equipment around or under vehicle

## Slide 8: More Walk-Around Watch Outs
Vehicles parked behind the engine
Personnel relaxing or sleeping around engine
Body damage while away from the engine
Cabinets latched and equipment secured
Side and overhead clearance in and near the path your vehicle will travel

## Slide 9: STOP Procedure

## Slide 10: “S”
Seat belts on?
  Seat belts must be available and used in Bureau motor vehicles.
  The driver is responsible for asking passengers if they are wearing their seat belts and ensuring they are worn at all times.

## Slide 11: “T”
Tools and equipment stowed?
  Ensure all tools and equipment are secured in cabinets or approved storage areas before moving the engine.

## Slide 12: “O”
Operator (driver) and crew has situational awareness.
  Determine if the engine is clear of hazards.
  Never back up an engine without checking behind the vehicle.
  Utilize spotters whenever possible.

## Slide 13: “P”
Personnel accounted for?
  Ensure all personnel are account for and their locations are known.
  Communicate your intentions to all personnel before moving the vehicle.

## Slide 14: Engine Danger Zones

## Slide 15: Engine Danger Zones
When working in close proximity of a moving engine, there is an increased risk for an accident to occur.
Given the size of our engines and the environment we work in, operator “blind spots” or danger zones exist.

## Slide 16: Engine Danger Zones
Whenever possible, operate in the green zones.
  Offer visual contact with the operator.
Yellow zones are areas of limited visibility and mirror-use areas.
  Notify the driver when you are in these areas.

## Slide 17: Engine Danger Zones
Never work in red zones when vehicle is moving.
Notify operator prior to entering red zones.
Stay out of red zone where the operator has no visual.

## Slide 18: Engine Danger Zones
The red area in front of the engine extends 10 feet out from the front bumper.
You must have visual contact with the driver when working in front of the vehicle beyond the 10-foot range.

## Slide 19: Engine Spotter Usage
There are always blind spots around the engine.
Always use a spotter when another person is available.
If alone, get out and do a visual yourself.

## Slide 20: When to Use a Spotter
Backing up
Off-road pioneering
Hazardous conditions exist
Low vehicle clearances exist
Narrow/confined driving spaces exist

## Slide 21: Spotter Techniques
Spotters should have a clear line of sight to the driver. Spotter position should be:
  Forward movement: Outside the forward red zone on the driver side windshield
  Backing movement: Outside the rear red zone on the driver side mirror
Spotters and drivers should agree upon a common set of hand signals.

## Slide 22: Spotter Techniques
Spotters and drivers need to communicate on the planned action.
Spotter distance from the engine will depend on various situations at the time of the maneuver; however, visual contact between the spotter and the driver shall not be compromised.
If the driver loses sight of the spotter, the driver should stop immediately and determine the spotter’s location.

## Slide 23: Vehicle Operations and Recovery

## Slide 24: Mirror and Seat Adjustment

## Slide 25: Mud and Sand Areas

## Slide 26: Side Hills

## Slide 27: Gullies/Ditches

## Slide 28: Vehicle Recovery

## Slide 29: Winch Use

## Slide 30: Jump Starting

## Slide 31: BIA M-52 Remove Radio Fuse
Most M-52 Radios are Fused at the Battery.
Remove Fuse Before Jump Starting.
Failure Will Lead to Serious Radio Damage for the KNG M-Series Radios.
B/K (Old Style) are Less Vulnerable But Can Still Become Damaged.

## Slide 32: Portable Battery Jump Starter
Works on Model 52 engines
Inexpensive.
Easily Stored.
Does Not Need a Second (Jumper) Vehicle.

## Slide 33: Tire Changing and Jacking

## Slide 34: Towing and Being Towed

## Slide 35: Driving Safety
The crew depends on you!

## Slide 36: Follow Safe Driving Practices

## Slide 37: Following Other Vehicles

## Slide 38: Braking/Stopping Distance

## Slide 39: Blown Tire Technique
The goal in any rapid loss of tire pressure or “blowout” is to keep the vehicle balanced and controllable. Do not panic. Any over-reaction by the driver—including slamming on the brakes or abruptly removing your foot from the accelerator—can result in a loss of vehicle control.
What you should not do:
  Do not step on the brake.
  Do not abruptly release your foot from the brake pedal.
What you should do:
  Accelerate slightly or keep steady pressure on the accelerator pedal.
  Gently correct the steering as necessary to stabilize your vehicle and regain control. Look where you want the vehicle to go and steer in that direction.
  Once your vehicle has stabilized, slowly remove your foot from the accelerator pedal allowing the vehicle to slow on its own.

## Slide 40: Off-Road Driving

## Slide 41: Night Driving

## Slide 42: Backing

## Slide 43: Engine Placement

## Slide 44: Ingress and Egress

## Slide 45: Parking

## Slide 46: The Black

## Slide 47: Blind Spots

## Slide 48: Hazards
Pay attention to your surroundings!
What hazards do you see in this picture?

## Slide 49: What was in the picture . . .
Creek undercut the road bank
Narrow passage way
Various terrain and fuel types
Rolled engine!

## Slide 50: Rock Piles/Outcroppings

## Slide 51: Various Terrain and Fuel Type Changes

## Slide 52: Aircraft

## Slide 53: Wild and Domesticated Animals

## Slide 54: Poor Weather Conditions

## Slide 55: Wildland-Urban Interface

## Slide 56: Staying Alert

## Slide 57: Post Off-Road Inspection

## Slide 58: Driving Reminders

## Slide 59: Driving Reminders
More time can be made up by getting out of the station quickly than by speeding en route.
Keep your vehicle in top condition. Inspect it regularly.

## Slide 60: Driving Reminders
Never let distractions interfere with your driving.
Good drivers drive smoothly and with control, not recklessly or erratically.
A heavier piece of equipment will not stop as easily as a passenger car.

## Slide 61: Accidents do not “just happen”

## Slide 62: Cone Course Exercise

## Slide 63: Objectives
Describe and demonstrate the driver walk-around before moving a fire engine.
Describe the STOP procedure and how it relates to the driver when operating a fire engine.
Identify danger zones around fire engines and describe actions that can be performed to reduce risk in these areas.

## Slide 64: Objectives
Describe and demonstrate the start-up and shifting procedures an ENOP must perform when operating fire engines.
Identify hazardous driving situations and describe actions that can be performed to reduce risk.
Demonstrate on an established course fire engine handling and maneuvering capabilities.