## Slide 1: Water Handling Operations
Unit 4C - Foam and Foam Proportioning Equipment

## Slide 2: Objectives
Discuss why foam is more effective than plain water when performing wildland fire suppression operations.
Discuss foam safety, including guidelines for handling foam products.
Identify and discuss the advantages and disadvantages of two manual foam proportioning methods used when performing wildland fire suppression operations.

## Slide 3: Objectives
Identify various operational components of the FoamPro® 1600/1601 and Waterous Aquis 1.5.
Demonstrate the ability to set up, run, have foam solution pumped to a nozzle person, and shut down a foam proportioner.

## Slide 11: Safety equipment

## Slide 13: Foam Proportioners

## Slide 14: Manual Foam Proportioners
Operators manually adjust the device to maintain a constant mix ratio when water flow and pressure changes.
  Cannot maintain constant mix ratio over various flow and pressure rates

## Slide 15: BIA M-52 Foam Flo
Simple and Effective.
Uses Standard Fittings and is Unpowered.
Can Get Foam Into Tank if Valving is Not Correctly Installed or if Internal Check Ball Malfunctions.

## Slide 16: BIA M-52 Foam FLo Off Position
Notes: Proportioner is graduated from Off to E. A is the lowest setting, E is the highest. Adjust to nozzle operators desired foam output. A Foam Flo will not automatically adjust for pressure or volume, the ENOP must do this manually.

## Slide 17: Foam On/off valve at tank
Notes: On/ Off Valve to foam tank. Must be opened to flow foam.

## Slide 18: Foam Proportioner inlet Valve -Off Position
Notes: This photo is input from the foam tank to foam proportioner. This valve must also be in the open position to flow foam.

## Slide 19: Model 52 Foam-flo
Water is Pushed Into the Unit From the Pump Side (LEFT SIDE)
Flows Across the Proportioner Valve and Pulls Concentrate Into a Mixture of Water and Concentrate.
Exits in Solution Above the Overboard Discharge Valve #3 (Right Side).
Notes: Most BIA M-52's discharge into a single Overboard Pipe. If this pipe is plumbed to part of the system that can uptake water into the pump head (common on BIA Model 52's) and the Recirculation Valve is open (#17), you will pump foam into the tank. This is a common issue and can lead to all sorts of problems. One of the discharge valves needs to be cracked open in order prevent foam from going the into the water tank. Review the foam valving on all BIA M-52's and correct as needed. View is top of Foam Pro.

## Slide 20: Batch Mixing

## Slide 21: Suction-Side Proportioners

## Slide 23: Automatic Foam Proportioner
The automatic foam proportioner makes an adjustment on its own to maintain a constant mix ratio when water flow and pressure changes.
Waterous Aquis™ 1.5
FoamPro® 1601

## Slide 24: Foam Proportioner
s

## Slide 25: Foam Proportioner
Proportional and automatic
Works on discharge side of pump
Class A foam only
Requires water flow and electrical current
No restrictions due to hose length or number of nozzles
No loss of pressure or flow
Accurate at all flow ranges
Resupply foam without interruption

## Slide 26: Operating the Foam Proportioner Major Components
Operator control module
Motor driver box/module
Paddlewheel flowmeter
Foam pump and electric motor
Calibrate/Inject valve
Inline strainer

## Slide 27: Operator Control Module Panel Mounted
Operating instructions
On/Off switch
Injection rate control
  Adjustable from 0.1%-1.0%
Low concentrate (“LOW CONC.”) light

## Slide 28: Motor Driver Box/Module Normal Operation
Circuit breaker switch “Up” for normal operation
Simulated flow switch “Down” for normal operation

## Slide 29: Paddlewheel Flowmeter

## Slide 30: Foam Pump and Electric Motor

## Slide 31: Calibrate/Inject Valve

## Slide 32: Purging Air
Enter “Simulated Flow”
  Switch to “Up” position
  Preprogrammed for 100 gpm
Valve to “Cal/Flush”
Turn panel switch “On”
Run pump until concentrate flows from dump line

## Slide 33: Purging Air Continued
Turn control panel to “Off” position
Return valve to “Inject”
Exit “Simulated Flow” by returning switch to “Down” position

## Slide 34: Inline Strainer

## Slide 35: Foam Injection Check Valve and Injection Port

## Slide 36: Objectives
Discuss why foam is more effective than plain water when performing wildland fire suppression operations.
Discuss foam safety, including guidelines for handling foam products.
Identify and discuss the advantages and disadvantages of two manual foam proportioning methods used when performing wildland fire suppression operations.

## Slide 37: Objectives
Identify various operational components of the FoamPro® 1600/1601 and Waterous Aquis 1.5.
Demonstrate the ability to set up, run, have foam solution pumped to a nozzle person, and shut down a foam proportioner.